## Slide 1: VisSched: An Auction based Scheduler for Vision Workloads on Heterogeneous Processors
Diksha Moolchandani*, Anshul Kumar*,
José F. Martínez¥, and Smruti R. Sarangi*
*Indian Institute of Technology Delhi, India
¥Cornell University, Ithaca, NY, USA
Contact: diksha.moolchandani@cse.iitd.ac.in

## Slide 2: Outline
Problem Motivation
Background and Related Work
Characterization of Workloads
Our Approach
Results
Conclusion

## Slide 3: Problem Motivation
Emergence of mobile/IoT/edge computing
AR/VR headset
Smart glasses
Smart door lock with
face recognition
Smart watch with camera
Emergence of new types of benchmark suites

## Slide 4: Problem Motivation
Similar workloads share a lot of common code kernels, eg: convolution
Face Recognition
Object Detection
Super resolution

## Slide 5: Problem Motivation
Limited compute capability of IoT Offload to cloud
FPGA
GPU
Multicore
Conventional way to accelerate vision workloads
No efficient techniques for handling multi-application concurrency

## Slide 6: Overall Design
W1
W2
S
B
S
B
S
S
Big core
Small core
S
B
K Resources
N Workloads
W3
W4
W5
W6
W7
W8
W10
W11
W12
W13
?
?
?
N>K
Auction Theory is the choice

## Slide 7: Our Approach
Specialized scheduling algorithms
Exploit the correlation among the phases of the workloads
Store precomputed bidding strategies for each phase and the current state of the workload – pattern table
Auction Controller
HW Structures
Memory
Multicore
B
L2 Cache
B
B
B
B
B
S
S
S
S
S
S
S
S
S
S
Big core
Small core
S
B
Pattern Table
HW Scheduler

## Slide 8: Outline
Problem Motivation
Background and Related Work
Characterization of Workloads
Our Approach
Results
Conclusion

## Slide 9: Nash Equilibrium
Stable operating point
  No player can unilaterally change its strategy without getting worse off
  Multiple such points can exist
  Choose the one that maximizes the aggregate utility (sum of individual utilities of all the players)

## Slide 10: Auction Theoretic Formulation
wallet2
wallet1
bid1
bid2
Bob
Alice
If bid2 > bid1 and bid2 = wallet2,
Alice will have an ice cream and zero money
If bid2 > bid1 and bid2 > wallet2,
Alice will have an icecream and a debt
If bid2 > bid1 and bid2 < wallet2,
Alice will have an icecream and some money
If bid2 < bid1,
Alice will not get the ice cream
Thus bid proportionally,
Bid =  * Wallet (W), 0 <  < 1
Some children get more happy with the ice cream, some need it more, some just throw it half
Complicate the scenario. Deduct a fee from their wallet
Bid =  * (W-F), F is the auctioneer’s fee

## Slide 11: Auction Theoretic Formulation
A1
A2
Auction
wallet1
wallet2
bid1
bid2
Winner
Unlike Bob-Alice’s one time ice-cream purchasing competition, scheduling has multiple such competitions at every scheduling quantum
B is the winner’s bonus to incentivize the players to bid
L is the loser’s subsidy to prevent starvation
()
Need to incentivize the players to bid in the current round, else they will keep saving the wallet money for future

## Slide 12: Strategy Calculation
A1
A2
Auction
wallet1
wallet2
bid1
bid2
Winner
If the distributions for (W-F) and B are same and uniform, a unique global Nash Equilibrium exist. For N bidders:
For different distributions, the strategies are calculated using Monte Carlo simulations accelerated with AI techniques

## Slide 13: Related Work
Technique | Functionality
SLICC [Atta et al. 2012] | Exploits the similarity of code based on i-cache footprints
CAMP [Saez et al. 2010] | Accelerates the applications that get maximum speedup for fast cores
BIS [Joao et al. 2012] | Accelerates the bottlenecks (leading to maximum number of wait cycles) on big cores
UBA [Joao et al. 2013] | Accelerates bottlenecks and lagging threads such that reduction in total execution time is maximized
AdaMD [Basireddy et al. 2019] | Accelerates the underperforming applications determined using an ML model
COLAB [Yu et al. 2020] | Finds core affinity of application and schedules on the basis of bottlenecks ensuring fairness by adjusting scheduling time slice

## Slide 14: Outline
Problem Motivation
Background and Related Work
Characterization of Workloads
Our Approach
Results
Conclusion

## Slide 15: Experimental Setup
Parameter | Value
Cores | 10 small + 6 big
Frequency | 1.55 GHz & 3.1 GHz
L1 I/D Cache | 32 KB, 64 bytes block size, associativity 4
Shared L2 | 256 KB per bank, 16 banks, 64 bytes block size, associativity 8
Memory
Multicore
B
L2 Cache
B
B
B
B
B
S
S
S
S
S
S
S
S
S
S
Big core
Small core
S
B

## Slide 16: Benchmarks
MEVbench Suite
CortexSuite
SD-VBS
7 multi-threaded (Sift, Surf, KNN, SVM, HoG, ORB, FAST), 4 single-threaded (Boost, ObjRec, FaceDet, AugRel)
Motion Estimation, PCA, RBM, Image Segmentation, Speech Recognition
Image Stitching, Texture Synthesis, Disparity, Localization, MSER, Feature Tracking

## Slide 17: Characterization of Workloads
Use the instruction mix in an execution interval as a feature vector
Perform clustering
Any interval belongs to one of the five clusters
The clusters are named on the basis of the dominant instructions in the intervals

## Slide 18: Characterization of Workloads
Average Silhouette score=0.8 implies the samples are correctly classified
Strong positive correlation between the same phases across different applications

## Slide 19: Outline
Problem Motivation
Background and Related Work
Characterization of Workloads
Our Approach
Results
Conclusion

## Slide 20: Overall Design
Cores are partitioned between OS scheduler and HW scheduler
Scheduling Granularity: 31.25-62.5 s
Context Sw. overheads in OS: 44.1-1496 s
Context Sw. in HW: 67 ns
HW Scheduler:
2 queues, running and ready queue
PC and register state
Invokes the auction controller for scheduling
Scope of this work

## Slide 21: Overall Design
W1
W2
S
B
S
B
S
S
Big core
Small core
S
B
K Resources
N Workloads
W3
W4
W5
W6
W7
W8
W10
W11
W12
W13
?
?
?
N>K
ALU
MEM
ALU
SSE
SSE
ALU
MEM
SSE
SSE
MEM
ALU
ALU

## Slide 22: VisSched: Flow Chart
Create phase table: phase-to-core mapping
Auction core c among the threads in its waiting queue
Predict the next phase for thread t & enqueue it in the appropriate waiting queue
Is scheduling
quantum of thread t on core c exhausted?
Schedule thread t to core c
Yes
Winner thread t

## Slide 23: Phase-to-Core Mapping
Phase | Core
SSE | C1 C2 C5 C7
ALU | C8 C9 C11 C12
MEM | C13 C3 C4 C6
NET | C10 C14 C15 C16
Phase Table
Provide an initial phase to core mapping for all the phases
Recomputed at every 100 M cycle interval. Smaller intervals lead to frequent cache misses
Heuristic: relative proportion of the executed phases (s : n : m : c), where s , n , m , c are the mapping counters
Stored as 16 bits per row, one bit corres. to each core

## Slide 24: Predicting the Next Phase
Condition | Inference
> | Memory Phase
> | SSE Phase
Default | Compute Phase
System call invocations | Network Phase
Condition | Inference
 | Memory Phase
 | SSE Phase
Default | Compute Phase
System call invocations | Network Phase
, , A, are the phase counters for counting the instructions of a phase
Additional priority to memory instructions because they involve multiple operations (addition+memory)

## Slide 25: Auction Process
Terms | Symbols | VisSched
Wallet | W | W
Auctioneer's fee | F |  * C
Bid | µ * (W - F) | µ * (W -  * C)
Bonus | B |  * IPC/Energy + Wbase
Loser's subsidy | L | L =  * Wbase
Updating the metrics | Winner | Loser
Utility | (1 - µ)(Wold - F) + B | 0
Wallet (Wnew) | (1 - µ)(Wold - F) + B | Wold + L
Symbol | Meaning
Wbase | Base Wallet balance
C | Migration cost calculated as a function of cache misses
IPC | Instructions per cycle
Energy | Energy consumed by the system
, ,  | Normalization constant
µ | Bidding Strategy
Wnew | Wallet balance in next auction round
Wold | Wallet balance in prev. auction round

## Slide 26: Auctioneer’s Fee (F)

## Slide 27: Winner’s Bonus (B)
Intuitively it should be IPC, it is the derived advantage that a thread gets if it gets access to the core
Good metric for homogeneous system, but biased for heterogeneous system, favors big cores
Average energy usage in small cores is 60-70% lower than big cores
Use IPC/Energy: unbiased, positively correlated with IPC (0.8-0.99)

## Slide 28: Bid, Wallet Balance & Loser’s Subsidy
()
is the bidding strategy
= for the winner
Note: Loser is given a subsidy to prevent its starvation and ensure that after a bounded time it is able to win an auction

## Slide 29: Auction Controller
Upon phase change, the wallet of the thread in the wallet table is updated with the bonus
Hardware Scheduler
New phase of the thread is calculated using the phase counters, and enqueued in the ready queue of the mapped core obtained from the phase table
Get the threads in the ready queue of the freed core, calculate their miss costs, calculate the new wallet balance and get the bidding strategy from the pattern table

## Slide 30: Pattern Table (PT)
Core-type
R
C
#n
Ph_id1..................Ph_idn
1 ...................... n
rebid
No of bidders
Phase ids of n bidders
Bidding strategy
Store pre-computed bidding strategies (1... n) in a lookup table
Requires to store the bidding strategy for every possible combination of bidders (W-F and B) rows of PT
Exploit the direct correlation of phases with the distributions of W-F and B
Note: 2- bit phase id (for 4 phases) can be used to identify the valuation of a bidder

## Slide 31: Filling the Pattern Table (PT)
Default PT
New B and W-F distributions
New PT
Dist. converged?
Collect samples
of B and W-F
PT generation
algorithm
No
Stop
Default PT stores =0.5 for all the combination of bidders
Collect 1000 samples of valuations and bonus
Find Nash equilibrium for all possible combinations of distributions in the PT
Yes
Start at a random solution having utility
Perturb each i, one at a time keeping others constant
For i if then calculate deviation
Calculate divergence
Stop when
= 0
If all the n bidders have same phase, then
else

## Slide 32: Outline
Problem Motivation
Background and Related Work
Characterization of Workloads
Our Approach
Results
Conclusion

## Slide 33: Results: Performance & ED2
Performance improvement 17%
ED2 improvement 14%

## Slide 34: Results: Fairness
=
)
Fairness for VisSched: 0.6
Nearest competing technique: 0.49
0.49

## Slide 35: Results: Hill Climbing
Characterize the search space of the strategies of the bidders
Mostly convex with small bumps; non-convexity ratio <= 5.6%
Use hill climbing to reach a minima
2-bidder case
4-bidder case
For 4-bidder case, each point is the best configuration of (3, 4)
For the 2-bidder case, two minima exist: N1(0.52, 0.37) and N2 (0.0.2, 0.02)
Need to find the non-trivial minima at N1

## Slide 36: Results
Configurations (6fc, 10sc) and (4fc, 12sc) are the Pareto optimal configurations in both the schemes
Red line is the Pareto optimal front: no other configuration uses lower energy for the same slowdown

## Slide 37: Results: Sensitivity
Sensitivity of VisSched w.r.t. small and big core counts
(10sc, 6fc), and (9fc, 7sc) in the Pareto front
The top leftmost point (10sc, 6fc) is optimal both in terms of ED2 and performance

## Slide 38: Results: DVFS
Power constraint is defined for each thread
Scheduling granularity of VisSched: 31.25 s
Time to switch between DVFS levels: 30-40 s
Switch DVFS level when the thread has executed on the same core for 3 consecutive intervals
19%
24%
2W per thread
4W per thread

## Slide 39: Results: Generality
40-60% same phase auctions in CortexSuite: 40% perf. improvement
20-40% same phase auctions in MEVBench: 17% perf. improvement

## Slide 40: Outline
Problem Motivation
Background and Related Work
Characterization of Workloads
Our Approach
Results
Conclusion

## Slide 41: Conclusion
Proposed a clustering-based technique to divide the execution intervals of a workload into phases
Demonstrated the correlation of phases across workloads
Proposed an auction-based starvation-free scheduling scheme where each thread has a replenishable virtual wallet to bid for cores
Used hill climbing to reach a Nash solution and store the bidding strategies of the bidders in the pattern table
17% performance improvement & 14% ED2 improvement
Proved the generality of the scheme and extended it for DVFS and custom accelerator