## Slide 1: pTask: A Smart Prefetching Scheme for OS Intensive Applications
Prathmesh Kallurkar, Smruti R. Sarangi
Indian Institute of Technology Delhi

## Slide 2: Outline of the talk
Introduction
Characterization of OS intensive applications
Results
Design of our prefetching technique ‘pTask’

## Slide 3: Why Instruction Prefetching for OS Intensive Applications
Non-privileged: Application
Privileged: OS
Parse web
request
Read
System call
Write
System call
Create
page
Time
Each task has a different instruction footprint.
Combined size of instruction footprints of all tasks is larger than the instruction cache
System call
Application
Interrupt

## Slide 4: Why another instruction prefetcher
 | Proactive Instruction Fetch (MICRO’11) | Return Address Directed Prefetching (MICRO ‘13)
Prefetch operation | All the time | All the time
Hardware overhead | 200 KB per core | 64 KB per core
Software overhead | None | None
Performance Improvement | 20.51 % | 19.78 %
Storage overhead of additional structures would make it difficult for the deployment of such sophisticated prefetchers in real systems

## Slide 5: What are we proposing
 | Proactive Instruction Fetch (MICRO’11) | Return Address Directed Prefetching (MICRO ‘13) | pTask (MICRO ‘16)
Prefetch operation | All the time | All the time | Certain points in the code
Hardware overhead | 200 KB per core | 64 KB per core | 72 B per core
Software overhead | None | None | OS routines
Performance Improvement | 20.51 % | 19.78 % | 27.38 %
pTask uses in-memory data structures to store the prefetch information

## Slide 6: Apache: Variation in i-cache hit rate
Tasks: system call handlers, interrupt (top half and bottom half) handlers, scheduler, applications
i-cache hit rate drops mostly when we switch from one task to another
Crux of our technique:
Do not run prefetching all the time
Prefetch only when transitioning from one task to another

## Slide 7
Non-privileged: Application
Privileged: OS
Time
Identify prefetchable execution blocks
OS Events
1) System call
2) Interrupt (top-half)
3) Interrupt (bottom-half)
4) Schedule routine
Execution block of 125 functions
HyperTask
libC functions that perform system call
Core functionality of OS tasks

## Slide 8: HyperTasks
System Execution
Application
(Execution between two system calls)
OS
Parse query
Create reply
System call
Interrupt
Bottom Half
Scheduler
Read file
Page fault
SCSI
schedule()

## Slide 9
Profile
Normal
Overview of the scheme:
Record the execution pattern of the HyperTask and find the list of frequently accessed functions.
Prefetch the HyperTask’s frequently accessed functions into the i-cache before executing it
Leverage repetitive execution pattern for prefetching
Time
Slower than baseline 
Faster than baseline 

## Slide 10: Outline of the talk
Introduction
Characterization of OS intensive applications
Results
Design of our prefetching technique ‘pTask’

## Slide 11: Benchmarks
Network:
  1) Apache: Web server (Apache)
  2) ISCP: Secure copy file from remote machine to local machine (SCP)
  3) OSCP: Secure copy file from local machine to remote machine (SCP)
Database:
  4) DSS: Decision Support System (TPCH: Query 2)
  5) OLTP: Online Transaction Processing (Sysbench benchmark suite)
File system
  6) Find: Filesystem browsing (Linux utility application Find)
  7) FileSrv: Random reads and writes to file (Sysbench benchmark suite)
  8) MailSrvIO: Imitate file operations of a mail server (Filebench benchmark suite)

## Slide 12: Instruction break up
20% for Oscp
90% for FileSrv
Interrupt handlers
(top-half and bottom-half)
should also be considered for
Instruction prefetching

## Slide 13
Break-up of i-cache’s hit rate and evictions
13/40
i-cache hit rate: OS intensive applications (80-90%) SPEC/PARSEC (>99%)
Most i-cache evictions occur because of inter-HyperTask competition
hit rate
breakup of evictions

## Slide 14
Challenge 1: Which functions should be prefetched?
a
b
c
d
e
f
g
h
i
j
Start:
: End
100 % (10/10)
90 % (9/10)
10 % (1/10)
10 profile runs
Classes of functions based on their frequency in profile runs:
a
b
c
d
e
f
j
g
h
i
9/10 profile runs
1/10 profile run

## Slide 15
Challenge 1: Which functions should be prefetched?
a
100 % (10/10)
90 % (9/10)
10 % (1/10)
Classes of functions based on their frequency in profile runs:
b
c
d
e
f
j
g
h
i
Prefetch all functions (>0%)
Advantage: Will be able to prefetch most functions
Disadvantage: Many prefetch operations may remain unused
Prefetch functions that were
called in all profile runs (100%)
Disadvantage: Will be able to prefetch limited number of functions only
Advantage: Most of the prefetch will be used

## Slide 16
Choose P50
16/40
Coverage =
#accessed lines found in prefetch list
#lines accessed by the HyperTask
Utility =
#lines in prefetch list that were accessed
#total lines in the HyperTask
PX=prefetch functions that were accessed in x% of the invocations
What we want -> High Coverage and High Utility
Challenge 1: Which functions should be prefetched?

## Slide 17: Challenge 2: How many times should we profile?
After 10 profile runs, JaccardDistance < 0.005
Create a Prefetch list at the end of each profile run
Plot the JaccardDistance between the Prefetch lists created at the each of consecutive profile runs

## Slide 18: Outline of the talk
Introduction
Characterization of OS intensive applications
Results
Design of our prefetching technique ‘pTask’

## Slide 19: Execution Model With pTask routines
pTask routines are called before starting each HyperTask

## Slide 20: Outline of the design section
Profiling
Prefetch list
HyperTask annotation
Normal mode
Recording functions in a single execution
Function annotation in OS and application executables

## Slide 21: Function annotation in OS and Application executables
Function foo () {
….
}
Function bar() {
…
}
Function foo () {
recordFunc 0
….
}
Function bar() {
recordFunc 1
…
}
Add marker instruction to each function
Add header to each executable
(Function Map)
Function IDx | Start address | #Lines
0 | 0x345 | 4
1 | 0x349 | 5

## Slide 22: Profiling: Recording Function Execution
0 | 0 | 0 | 0 | 0 | 0 | 0
Function Vector
(stored in memory)
No. of functions in the executable
All bits are set to ‘0’ at the start of a profile run
Function call sequence:
foo(): recordFunc 0
Set bit number 0
1 | 0 | 0 | 0 | 0 | 0 | 0
func(): recordFunc 5
Set bit number 5
1 | 0 | 0 | 0 | 0 | 1 | 0
Bit of each executed function should be set to ‘1’ at the end of profile run

## Slide 23: Outline of the design section
Profiling
Prefetch list
HyperTask annotation
Normal mode
Identifying application HyperTasks
Identifying OS HyperTasks

## Slide 24: Identifying Application HyperTasks
Application HyperTask: user process’ execution between two system calls
Encode the sequence of functions called by the user process between two system calls
recordFunc n
pathVec[i] = 1
pathVec[i]
== 0
Y
pathSum += i
pathSum (left-shift) i
Captured using two 256-bit registers: pathSum and pathVector
i = n % 256

## Slide 25: Identifying OS HyperTasks
System calls:
Read system call
Network socket
Disk file
Both versions have different instruction sequences
How to differentiate at run-time:
Use ID of the application HyperTask that executed just before the system call
Naïve approach: Use system call ID (as defined by the OS developer)
Write system call

## Slide 26: Identifying OS HyperTasks
OS HyperTasks
System call handler
Interrupt handler
Bottom half handler
Scheduler
ID of the previous application HyperTask
Interrupt ID
Program counter of the bottom half handler’s routine
Add special instruction at the beginning of schedule()

## Slide 27: Outline of the design section
Profiling
Prefetch list
HyperTask annotation
Normal mode
Profile store
Prefetch store

## Slide 28: Profile Store
0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1
Function Vector
(End of profile run)
Profile Store
(in-memory)
Increment frequencies of functions 3,6,9
HyperTask ID | #Profile runs | Function frequency list
H1 | 1 | (3→1) (6→1) (9→1)

## Slide 29: Prefetch Store
HyperTask ID | #Profile runs | Function frequency list
H1 | 10 | (3→10) (6→2) (8→7) (9→9)
Choose functions that satisfy P50 criteria
3, 6, 9
Functions deemed to be frequent
for HyperTask H1:
HyperTask ID | Prefetch list (run-length encoding)
H1 | (0x695, 3) (0x734, 2) (0x789→4)
Profile Store
(in-memory)
Prefetch Store
(in-memory)

## Slide 30: Outline of the design section
Profiling
Prefetch list
HyperTask annotation
Normal mode
Issue prefetch operations
Re-profiling

## Slide 31: Normal mode
Step 1: Locate prefetch list and issue prefetch operations
Step 2: Execute HyperTask
recordFunc instruction:
Treat as NOP for OS HyperTasks
Update application taskID
Execute HyperTask
HyperTask boundary

## Slide 32: Re-profiling
(Avg. miss rateold – Avg. miss ratenew) > 8%
Re-profile HyperTask if:

## Slide 33: Outline of the talk
Introduction
Characterization of OS intensive applications
Results
Design of our prefetching technique ‘pTask’

## Slide 34: Evaluation Setup
Native OS
QemuTrace
Guest OS
(Linux 2.6.32)
Benchmark
Execution
Traces
Tejas

## Slide 35: Hardware Details
Parameter | Value
Cores | 16
Pipeline | Out Of Order Pipeline
Private cache | i-cache (4-way 32 KB), and d-cache (4-way 32 KB)
Shared cache | L2 cache (8-way 4 MB)
OS | Linux 2.6.32 (Debian 6.0)

## Slide 36: Evaluated Techniques
Technique | Granularity | Hardware overhead
Markov [MICRO’05] | i-cache line | 4 KB per core
Call Graph Prefetching [TOCS’03] | Functions | 32 KB per core
Proactive Instruction Fetch [MICRO’11] | Stream of instructions | 200 KB per core
Return Address Directed Prefetching [MICRO’13] | Functions | 64 KB per core
pTask [proposed] | Next HyperTask | 72 B per core

## Slide 37
Performance Comparison
37/40
pTask outperforms
state of the art
prefetchers
by 6-7%

## Slide 38
38/40
Breakup of
i-cache accesses:
Low iWaitPrefetch
  Prefetch opns complete before the line is accessed
High iHit
  Able to predict the execution patterns better

## Slide 39: Conclusion
Proposed pTask, an instruction prefetcher that is optimized for OS intensive workloads
Basic insights:
  Prefetch only when transitioning from one task to another
  Turn off prefetching for steady phase of execution when i-cache hit rates are high
Demonstrated an average increase in instruction throughput of 7% over highly optimized instruction prefetching proposals for a suite of 8 OS intensive applications

## Slide 40: Questions