## Slide 1: HAJPAQUE: Hardware ACCELERATOR FOR JSON PARSING, QUERY PROCESSING AND SCHEMA VALIDATION
SAMIKSHA AGARWAL AND SMRUTI R. SARANGI
SCHOOL OF INFORMATION TECHNOLOGY
INDIAN INSTITUTE OF TECHNOLOGY DELHI, INDIA

## Slide 2: Outline
Motivation
Background
Design Proposal
Evaluation
Comparison with Existing work
Conclusion

## Slide 3: MOTIVATION: WHY JSON PARSING IN H/W
Increasing popularity of JSON over XML (more readable and memory - efficient)
  SW parsers offer best case throughput of 20 Gbps  performance bottleneck
  SW parsers’ throughput is highly sensitive to the nature of JSON data and queries
  Heavily used in real time analytics supporting throughputs > 50Gbps
1. Image Source: http://realpython.com/python-json/
1.
2. Image Source: http://blog.axway.com/apis/why-json-won-over-xml
2.
Notes: Big data : Volume and velocity(streaming new data)
Real time analytics is the discipline that applies logic and mathematics to data to provide insights for making better decisions quickly. Source of real-time data can be sensors, IoT devices or web requests(twitter).

## Slide 4
SCALABLE
ROBUST
FAST
1. Image Source: http://www.sumuforex.com/p/forex-sinhala-advantages-of-forex.html
1.

## Slide 5: Outline
Motivation
Background
Proposal
Evaluation
Comparison with Existing work
Conclusion

## Slide 6: BACKGROUND: JSON (JavaScript Object Notation)
Format for representing semi-structured data
Collection of objects, where every object is an un-ordered set of key-value pairs.
{“Name”: “John”, “AGE”: 50, “Car”: NULL}
{“Name”: “Ray”, “AGE”: 45, “Car”: {“attributes”: {“color”: Black, “electric”: Yes}}
{“Name”: “Mike”, “AGE”: 30, “Car”: {“Sedan”: [BMW, Mercedes], “SUV”: False}}
RECORD
(TOP-LEVEL OBJECT)
KEY
VALUE
NESTED OBJECT
VALUE ARRAY
Sample JSON document
TOKENS
{
:
,
}
[
]

## Slide 7: Background: JSON Query/SCHEMA
{“Name”: “John”, “AGE”: 50, “Car”: NULL}
{“Name”: “Ray”, “AGE”: 45, “Car”: {“attributes”: {“color”: Black, “electric”: Yes}}
Car.attributes.color
Name
John, Ray
Black
{
“type”: “object”,
“required”: [“NAME”, “AGE”, “Car”],
“properties”: {
“Name”: {
“type”: “string”
},
“AGE”: {
“type”: “number”,
“minimum”:0 ,
“maximum”:70
},
}
}
Query1
Query2
JSON Schema

## Slide 8: Outline
Motivation
Background
Proposal
Evaluation
Comparison with Existing work
Conclusion

## Slide 9: PROPOSAL: DESIGN CONSIDERATIONS
Reduce CPB
  Process 16 bytes in parallel : theoretically reducing CPB by 16 times.
  Penalty: More complexity, area and power
JSON
HAJPAQUE
16 bytes
Increase f
  Pipelined design
  Use of novel design techniques to reduce critical path length
f = operating design frequency
CPB = clock cycles per byte

## Slide 10: PROPOSAL: HAJPAQUE
Application
DOM
Constructor
Memory
Offline
Query
Processor
Stream Parser
Online
Query
Processor
Online
Schema
Validator
JSON
UTF-8 validation
Check-map construction & compaction
Key/Value address location, filtering & extraction
Depth-processing & Key-Value Pair creation
Stream Parser
Block Diagram : HAJPAQUE

## Slide 11
STEP1: UTF-8 VALIDATION
Byte No.
B0
B1
B2
B3
B4
B5
Byte Type
Leading
Continuation
Continuation
Leading
Leading
Continuation
Character
Length
3
1
1
1
2
1
Byte No.
B0
B1
B2
B3
B4
B5
Byte Type
Leading
Continuation
Continuation
Leading
Leading
Continuation
Character
Length
3
1
1
2
2
1
Error Recovery: The erroneous leading byte and the corresponding continuation bytes (if any) are excluded from further processing.
There are two types of bytes used in the UTF-8 encoding technique: leading byte and continuation byte.
The leading byte has the information about the length of the character.

## Slide 12
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
“ | K | 1 | ” | : | V | A | L | 1 | , | “ | K | 2 | ” | : | V
1 | 2 | 1 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 3 | 10 | 13 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 2 | 0 | 0
JSON Set
Check-Map
Type CCM
Position CCM
Byte No.
Check-Map builder
Compaction engine
Step2: KEY-VALUE LOCATOR
QUOTE
QCOLON
QUOTE
QCOLON
1 | 2 | 1 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 3 | 10 | 13 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Key
Value
Key
Type CCM
Position CCM
Type of field
Key-Value locator
Parallel sliding Window based approach
Notes: Each pair of consecutive CCM entries are examined to determine the type of JSON field.
The position CCM is used to determine the start and end address of the identified JSON field.
The compaction of the check-map allows us to apply the sliding window in parallel; hence shortening the critical timing path.

## Slide 13
STEP3: KEY-VALUE FILTERING AND EXTRACTION
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
“ | K | 1 | ” | : | V | A | L | 1 | , | “ | K | 2 | ” | : | V
“ | K | 1 | ” | : | { | “ | K | 2 | “ | : | V | A | L | 2 | ,
“ | K | 1 | ” | : | V | A | L | 1 | } | { | “ | K | 2 | “ | :
The incomplete keys/values in a set are buffered and are read out when the key/value completes in the next cycle.
Error Recovery in case of buffer overflow: The key or the value that caused the buffer to overflow, is excluded in its entirety from further processing
The value might contain a few structural tokens like the comma or curly braces; they need to be filtered out.
Token i | Token i+1 | Type of enclosed field
QCOLON | QUOTE | VALUE
QUOTE | QUOTE | VALUE
QUOTE | QCOLON | KEY

## Slide 14
Compaction engine
Field relationship
Step4: KEY-VALUE PAIR CREATION/relationship builder
KEY | 0 | 0 | KEY | 0 | 0 | 0 | 0 | 0 | 0 | VALUE | 0 | 0 | 0 | 0 | 0
Pair Array
Parallel Sliding Window based approach
KEY | KEY | VALUE | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Compacted Pair Array
Key-Value Pair
1st key is the parent of 2nd key ; 2nd key is child of 1st key
1ST key is “Non-Terminal” key
2nd key is “Terminal” Key
Parent child relationship among 2 keys, if and only if depth(parent key) depth(child key) -1
Key-Value pair if and only if depth(key) = depth(value)

## Slide 15: DEPTH CALCULATION
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
{ | “ | K | 1 | “ | : | { | “ | K | 2 | “ | : | V | 1 | } | }
1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 2
1 | 1 | 2 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 6 | 14 | 15 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Byte No.
JSON Set
Check-Map
Type CCM
Increment depth whenever a ‘{‘ is encountered, decrement depth whenever a ‘}’ is encountered.
D+1
D+2
D+1
Depth=D
D
Position CCM

## Slide 16: Online QUERY PROCESSOR
Query Tables
Query Matching engine
Online Query Processor
Car.attributes..electric??
VALID | KEY
1 | Car
1 | attributes
1 | electric
0 | 
0 | 
0 | 
0 | 
Query Table 1
Application
DOM
Constructor
Memory
Offline
Query
Processor
Stream Parser
Online
Query
Processor
Online
Schema
Validator
JSON
Query tables must be pre-programmed with the application queries.

## Slide 17: QUERY MATCHING ENGINE
Car.attributes. electric??
VALID | KEY | Match
1 | Car | 1
1 | attributes | 1
1 | electric | 1
0 |  | 
0 |  | 
0 |  | 
0 |  | 
If the match is due to a non-terminal key, the Valid bit of the succeeding entry of the Query Table must be ‘1’.
If the match is due to a terminal key, the Valid bit of the succeeding entry in the query table must be ‘0’, except if the match is for the last table entry.
Car.attributes.mileage??
VALID | KEY | Match
1 | Car | 1
1 | attributes | 1
1 | mileage | 0
0 |  | 
0 |  | 
0 |  | 
0 |  | 
Necessary checks:
Error Recovery: The query-match bits of all the entries of the query table are reset.

## Slide 18: SOLUTION
Car. color. attributes??
VALID | KEY | Match | Depth
1 | Car | 1 | 1
1 | color | 1 | 3
1 | attributes | 1 | 2
0 |  |  | 
0 |  |  | 
0 |  |  | 
0 |  |  | 
Use DEPTH information of the keys extracted from JSON data
If the Query Table has k valid entries,
Depth[i] = (Depth[i-1] + 1) where (i=0,1,...k-1)
What if the matching keys are not in the correct order??

## Slide 19: RESETTING MATCH BITS
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
C | a | r | “ | : | N | U | L | L | } | { | “ | N | A | : | V
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 2 | 0 | 0 | 0 | 0 | 0
1 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
9 | 10 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Start of New Record
Byte No.
JSON Set
Check-Map
CCM
Sliding Window
Reset Match bits whenever the starting point of a new record is detected

## Slide 20
Creation and Compaction of check-maps using lookup tables
Parallel application of sliding-windows for following tasks is responsible for achieved parallelism:
  Key-value location
  Key-value relationship building
  Depth calculation
We propose the HPQME (Highly Parallel Query Matching Engine) to achieve a high degree of parallelism:
  Every incoming key is matched with all entries of query table in parallel.
  The depth of the matching keys are analyzed using parallel application of 2-entry sliding window.
  Parallel application of sliding window to detect start of a new record: useful for both resetting query tables as well as schema table.
These techniques are generic in nature and can be utilized in any hardware design dealing with semi-structured data
NOVEL CONTRIBUTIONS
1. Image Source: https://nuts-about-needlepoint.com/october-new-needlepoint-products/
1.

## Slide 21: Outline
Motivation
Background
Proposal
Evaluation
Comparison with Existing work
Conclusion

## Slide 22: EVALUATION: SETUP
HDL : Verilog
Tools :
  HDL editor: Xilinx Vivado
  Simulator : Xilinx Vivado
  Synthesis: Synopsys DC
Target Device : ASIC
Technology: 28nm FDSOI
Corner: SSLVLT(worst for this technology)
Datasets
iris.json
Covid_features.json (YELP)
business.json (YELP)
twitter.json
  Standard datasets; vary in terms of (for a given size of dataset):
  Number of records
  Number of parsed fields
  Maximum depth of nested object in a record
  Standard queries chosen; vary in terms of frequency and depth of valid results

## Slide 23: EVALUATION: SYNTHESIS REPORTS
AREA (in um2) | 
Total | 292839
Combinational | 184097
Sequential | 108742
POWER ( in mW) | 
Dynamic | 43.3
Static | 0.008
DESIGN PARAMETER | VALUE
Number of query processors/tables | 1
Number of entries in the query table | 7
Width of a query table entry | 32 bytes
Number of entries in the schema table | 4
Width of schema table entry | 32 bytes
Maximum operating frequency = 833 MHz
HAJPAQUE is a 10 stage pipeline
Streaming parser contributes roughly 50% to the total area and power consumption and 80% to the total pipeline latency

## Slide 24: Evaluation: PERFORMANCE ANALYSIS
Size of dataset (twitter.json) | Total clock cycles | CPB | Throughput
100 B | 16 | 0.16 | 5.21 GB/s
1 kB | 72 | 0.072 | 11.57 GB/s
10 kB | 634 | 0.0634 | 13.14 GB/s
100 kB | 6250 | 0.0625 | 13.33 GB/s
0.6 MB | 37500 | 0.0625 | 13.33 GB/s
Size of dataset (twitter.json) | Total clock cycles | CPB | Throughput
100 B | 18 | 0.18 | 4.62 GB/s
1 kB | 79 | 0.079 | 10.54 GB/s
10 kB | 685 | 0.0685 | 12.16 GB/s
100 kB | 6789 | 0.0679 | 12.27 GB/s
0.6 MB | 40621 | 0.0677 | 12.30 GB/s
STREAM PARSING + ONLINE QUERYING
DOM PARSING
Throughputs saturate for datasets>10kB as fixed overheads of pipeline latency becomes insignificant
DOM parsing throughput < Stream-based parsing due to the memory accesses

## Slide 25: Outline
Motivation
Background
Proposal
Evaluation
Comparison with Existing work
Conclusion

## Slide 26: COMPARISON with state-of-the-art parsers
Feature | Rapidjson | Mison | Simdjson | HAJPAQUE
Stream Parsing |  |  |  | 
Online Querying |  |  |  | 
DOM Parsing |  |  |  | 
Offline Querying |  |  |  | 
UTF-8 encoding validation |  |  |  | 
Schema Validation |  |  |  | 
HAJPAQUE IS A FULLY-FEATURED JSON PARSER

## Slide 27: COMPARISON with state-of-the-art parsers
Parser | Parse DOM only | Parse + Scan DOM | Stream Parse + Online Querying
Rapidjson | 0.21 GB/s | 0.1 GB/s | 0.2 GB/s
Simdjson | 0.63 GB/s | 0.32 GB/s | 0.6 GB/s
HAJPAQUE | 12.3 GB/s | 7.5 GB/s | 13.33 GB/s
System:
Intel Core i7-8700 CPU @
3.20GHz
Query:
user.id
Dataset:
twitter.json (0.6 MB)
Roughly ~20X speedup as compared to Simdjson

## Slide 28: Outline
Motivation
Background
Proposal
Evaluation
Comparison with Existing work
Conclusion

## Slide 29: CONTRIBUTIONS
  Proposed integrated hardware solution for parsing; querying and schema validation of JSON
  Our design caters to a diverse class of applications; some of which rely on stream parsers and some on DOM parsers.
  Achieved a throughput of 13 GB/s, which is 5X-20X faster than existing software parsers.
  Processed 16-bytes together; offering significant much higher CPB as opposed to single byte per cycle approach
  Proposed novel design techniques like the sliding window-based field locator and the parallel query matching engine to achieve optimum operating frequency
  The stream parser’s performance is not affected by the nature of JSON data or JSON queries
  If we do not consider DOM-tree construction, then the rest of our online pipeline does not have any stalls

## Slide 30
Questions
Email: agarwalsamiksha94@gmail.com
Contact: +44 7435846807
Academic institution: IIT DELHI, India
Current Organization: Indie Semiconductor, Edinburgh, UK