## Slide 1: A Fast Leakage Aware Thermal Simulator for 3D Chips
Hameedah Sultan and Smruti R. sarangi
Computer Science and Engineering
Indian Institute of Technology Delhi, India

## Slide 2: Outline
Background
Popular techniques
Motivation for our Work
Steady State Thermal Simulator
Transient Thermal Simulator
Results

## Slide 3: Background

## Slide 4: Introduction
Quantify harmful effects on chip
  Mobility, speed
  Lifetime, reliability
  Interconnect Resistivity
Thermal Aware Design
  Optimization
  Floorplanning
  Cell Placement
Cooling System Provisioning
  Cabinet design and fan settings
Uses of
Thermal Simulator

## Slide 5: Thermal Simulator
Floorplan
DynamicPower Profile
Temperature Profile
.55 W
3 W
1 W
1 W
5 W
2 W
47
58
52
52
65
51
Thermal Simulator
Notes: Type equation here.
"Type equation here."

## Slide 6: Literature Survey
Finite Element
Finite Difference
Transform based
Galerkin Method
Approx. FEM
Thermo Electric Equivalence
Matrix Multiplication based
Computing the Green’s functions
Using pre-obtained Green’s fxn
Computation time decreases, accuracy decreases

## Slide 7: Finite Difference
Symbol | Meaning
 | Density
 | Specific heat
 | Temperature
 | Conductivity
 | Heat Generation Rate
Symbol | Meaning
 | Density
 | Specific heat
 | Temperature
 | Conductivity
 | Heat Generation Rate
Finite Difference

## Slide 8: Green’s Function
Green’s function
Temperature field of a unit impulse power source
𝑇=𝐺 ⊛ 𝑃
convolution operation

## Slide 9: Basic Idea
                Power Profile Green’s Function
                Temperature Profile

## Slide 10: How to find the Green’s function ?

## Slide 11: Transform based Approaches
Floorplan
DynamicPower Profile
Temperature Profile
Thermal Simulator
Apply a unit power source
𝑻=𝑮 ⊛ 𝑷
Measure the Green’s function, G
Apply a unit power source
Measure the Green’s function, G

## Slide 12: Power Profile
                Power Profile
Dynamic Power
Leakage Power
leakage at
ambient temp

## Slide 13: Leakage Power Modeling
BSIM4 Model:
Symbol | Meaning
 | Thermal voltage
 | Offset voltage
 | Drain to source voltage
 | Gate to source voltage
 | Constant
 | Threshold voltage
Symbol | Meaning
 | Thermal voltage
 | Offset voltage
 | Drain to source voltage
 | Gate to source voltage
 | Constant
 | Threshold voltage

## Slide 14: Popular Simulators – Hotspot [2], 3D–ICE [3]
Floorplan
Solve
Temperature
Trace
Calculate
using BSIM eqn
`
.55 W
3 W
1 W
1 W
5 W
2 W
.55
3
1
1
5
2
.05
0.3
0.1
0.1
0.5
0.2
Thermal Simulator

## Slide 15: Motivation for our work
Our focus: simulation speed in 3D chips
Very few techniques exist for 3D chips
Leakage power handled analytically
Prior work handles leakage iteratively
Transient temperature profile including leakage
No such transform based technique exists for 3D chips

## Slide 16: Work Done
Leakage Aware Thermal Simulator for 3D Chips
  Steady State Simulator
  Transient Simulator

## Slide 17: Floorplan of the chip
4 layers of Silicon
16 X 16 grid
.01 m X .01m X .00015m
16 Green’s functions
Assume source in layer 2
Source in layer j
Effect in layer i

## Slide 18: Linearity of leakage
We calculated the leakage power using the BSIM equation
  Leakage linearly dependent on temperature in the range 40-80
  Error limited to 1%.
Liu et. al (2007) and Sarangi et. al (2014) show similar results using HSPICE experiments

## Slide 19: Basic Idea of our Approach
Floorplan
Dynamic Power Profile
Temperature Profile
Thermal Simulator
Apply a unit power source
𝑻=𝑮 ⊛ 𝑷
Measure the Green’s function, G
Compute leakage aware Green’s functions
Apply a unit power source
Measure the Green’s function, G
Compute leakage aware Green’s functions
Offline
Online

## Slide 20: Computing the Leakage Aware Green’s Functions
Sarangi, S.R. et al., “LightSim : A Leakage Aware Ultrafast Temperature Simulator,” ASP-DAC, pp. 855-860, 2014.
Initially,
Apply impulse power source
Traditional approaches use 2D FFT
We convert 2D to 1D
Notes: (2)
𝑇=𝑓_𝑠𝑖𝑙𝑖𝑐+𝜅+𝛽𝑓_𝑠𝑖𝑙𝑖𝑐∗𝑇+𝜅_1 (2)

## Slide 21: Hankel Transform
2D Fourier transform of a radially symmetric function = 1D Hankel transform
  is a Bessel function of the first kind of order 0
Convolution in spatial domain = Multiplication in transform domain

## Slide 22: 2D Leakage Modified Green’s Function
Notes: Modified Green’s Functions With Leakage for 2D

## Slide 23: The Fundamental 3D Steady State Equations
Notes: = Temperature in layer i, because of source in layer j

## Slide 24: The Fundamental 3D Steady State Equations – Solution
Notes: = Temperature in layer i, because of source in layer j

## Slide 25: 3D Leakage Modified Green’s Functions
Compute the Hankel transform
Simplify and solve for H(T)
- Mathematica
Ignore second order effects
Compute the inverse Hankel transform

## Slide 26: Corrections for Edges and Corners

## Slide 27: Final Temperature Profile
Traditional approach:
𝑇=𝐺 ⊛ 𝑃
𝐹(𝑇)=𝐹(𝐺)𝐹(𝑃)
We save the Leakage modified Green’s functions in the transform domain itself
𝐻(𝑇)=𝐻(𝐺)𝐻(𝑃)
𝐻(𝑇)=𝐻(𝑇_12 )𝐻(𝑃_1 )+𝐻(𝑇_22 )𝐻(𝑃_2 )+𝐻(𝑇_32 )𝐻(𝑃_3 )+𝐻(𝑇_42 )𝐻(𝑃_4 )
Traditional approach:
We save the Leakage modified Green’s functions in the transform domain itself

## Slide 28: Other Techniques used for Edges and Corners
Some recent techniques [2] use the method of images
Our method achieves the same task without increasing the size of the P matrix.
Time taken for a convolution operation depends on the size of the matrices
Extend power dissipation matrix 9 times with mirror images.
Significant savings in the online part
A. Ziabari et al., “Power blurring: Fast static and transient thermal analysis method for packaged integrated circuits and power devices," VLSI Systems, IEEE Transactions on, vol. 22, no. 11, pp. 2366-2379, 2014.

## Slide 29: The Fundamental 3D Transient Equations

## Slide 30: The Fundamental 3D Transient Equations
We take the Hankel transform of the formulated set of equations and simplify.
Simplify
Take Laplace transform, interchange Hankel and Laplace transforms.
Formulate equations
The first few terms of the resulting equation correspond with the steady state temperature profile
The first few terms of the resulting equation correspond with the steady state temperature profile 〖(𝑇〗_12𝑠𝑠)
Perform further operations
Use transform properties
We take the Hankel transform of the formulated set of equations and simplify.
Simplify
Take Laplace transform, interchange Hankel and Laplace transforms.
Formulate equations
Perform further operations
Use transform properties

## Slide 31: The Fundamental 3D Transient Equations
Hankel transform
Take Laplace transform with respect to time and interchange Hankel and Laplace transforms.

## Slide 32: Transient Analysis
4 such equations for

## Slide 33: Approximations for transient analysis
Solve for , … and keep the effect of neighbouring layer only
Solve for 〖𝐿(𝐻(𝑇〗_12)), … 〖𝐿(𝐻(𝑇〗_42)) and keep the effect of neighbouring layer only
〖𝐻(𝑇〗_12)=〖𝐻(𝑇〗_12𝑠𝑠) − (〖𝐻(𝑇〗_22𝑠𝑠)𝑓_11 〖𝐻(𝑓𝑠𝑝〗_12)𝑒^(−𝑡/(𝑓_22 𝐻(〖𝑓𝑠𝑝〗_22))))/(𝑓_22 𝐻(〖𝑓𝑠𝑝〗_22))
Calculate the inverse transform of the above equation using the following approximations:
At high h,
At high h, (𝑓_11 〖𝐻(𝑓𝑠𝑝〗_12))/(𝑓_22 〖𝐻(𝑓𝑠𝑝〗_22)) ≃1.1
At low h, we neglect the leakage terms and assume
At low h, we neglect the leakage terms and assume 𝑓_(22 )=𝑓_(22 0)
Calculate the inverse transform of the above equation using the following approximations:

## Slide 34: Further speedup
Continuous Hankel transform involves performing costly integration operations.
We use the fast Discrete Hankel Transform algorithm proposed by Johnson [3] .
  where is the kth root of the Bessel function, and N is the defined range of the function whose Hankel transform has to be computed.
H. F. Johnson, “An improved method for computing a discrete hankel transform," Computer physics communications, vol. 43, no. 2, pp. 181-202, 1987.

## Slide 35: Further speedup: lookup table
To save computation time, we pre-compute all the roots of the Bessel function needed, and store it in a lookup table.
n | 
1 | 2.40482555769577
2 | 5.52007811028631
3 | 8.65372791291101
4 | 11.7915344390142
n | 
1 | 2.40482555769577
2 | 5.52007811028631
3 | 8.65372791291101
4 | 11.7915344390142

## Slide 36: Leakage Converged Transient Temperature Profile
Temperature changes at continuously with time => leakage power changes at every instant
To calculate leakage converged temperature profile in traditional simulators, we have to update leakage values at each instant, apply equivalent additional power and re-run the simulation.
We need to run a simulation for every time instant at which temperature values are needed => a very expensive process.

## Slide 37: Steady State Results
Steady state
Simulator | Execution time | Error (K) (From papers)
Ansys | 2-4 hours | --
Hotspot (HS3D) | 1.1s | 1.4
3D ICE | 1.1s [3] | 1.6
Our method | 0.016s | 1.5
Notes: Average error: 3.5%
Hankel transform of Green’s functions:
Calculation of leakage aware Green’s functions:
Online temperature profile calculation:
Average error: 3.5%
Hankel transform of Green’s functions: 0.96𝑠
Calculation of leakage aware Green’s functions: 85𝜇𝑠
Online temperature profile calculation: 16m𝑠

## Slide 38: Steady State Temperature Profile

## Slide 39: Transient Results
Error: <6%
Time for 100 points: 3.5s
71X speedup over 3D ICE

## Slide 40: Conclusion

## Slide 41: Thank you

## Slide 42: References
Sarangi, S.R. , Ananthanarayanan, G. and M. Balakrishnan, “LightSim : A Leakage Aware Ultrafast Temperature Simulator,” ASP-DAC, pp. 855-860, 2014.
Huang, Wei, Shougata Ghosh, Sivakumar Velusamy, Karthik Sankaranarayanan, Kevin Skadron, and Mircea R. Stan. "HotSpot: A compact thermal modeling methodology for early-stage VLSI design." Very Large Scale Integration (VLSI) Systems, IEEE Transactions on , vol. 14, no. 5, pp. 501-513, 2006.
A. Sridhar, A. Vincenzi, M. Ruggiero, T. Brunschwiler, and D. Atienza, “3D-ICE: Fast compact transient thermal modeling for 3D ICs with inter-tier liquid cooling," in ICCAD, 2010.
Zhang, Yufu, Ankur Srivastava, and Mohamed Zahran, "Chip level thermal profile estimation using on-chip temperature sensors." Computer Design, IEEE International Conference on. IEEE, pp. 432-437, 2008.
Zhan, Yong, and Sachin S. Sapatnekar. "High-efficiency Green function-based thermal simulation algorithms," Computer-Aided Design of Integrated Circuits and Systems, IEEE Transactions on, vol. 26, no. 9, pp. 1661-1675, 2007.
Francisco J. Mesa-Martínez,Joseph Nayfach-Battilana, Jose Renau ,”Power Model Validation Through Thermal Measurements,” In Proceedings of the 34th annual international symposium on Computer architecture (ISCA '07). ACM, New York, NY, USA, pp. 302-311,2007.
ANSYS ICEPAK 12.1, "User’s Guide." Fluent Inc (2009).
A. Ziabari, J.-H. Park, E. K. Ardestani, J. Renau, S.-M. Kang, and A. Shakouri, “Power blurring: Fast static and transient thermal analysis method for packaged integrated circuits and power devices," VLSI Systems, IEEE Transactions on, vol. 22, no. 11, pp. 2366-2379, 2014.

## Slide 43: References contd…
H. F. Johnson, “An improved method for computing a discrete hankel transform," Computer physics communications, vol. 43, no. 2, pp. 181-202, 1987.
I. Wolfram Research, “Mathematica," Illinios, 2012.

## Slide 44: Flow of our Algorithm
Obtain the temperature field by applying a unit power source ≡ Green’s functions
Modify the initial Green’s functions to obtain leakage aware Green’s functions
Convolve the Green’s functions with the power profile to obtain the temperature profile.