## Slide 1: Synopsis presentation of the proposed thesis Efficient On-Chip Optical Interconnects
Eldhose Peter (2013CSZ8108)
Guided by Dr. Smruti Ranjan Sarangi
Dept of CSE, Indian Institute of Technology, New Delhi, India
Efficient Optical
Interconnects

## Slide 2: What will be the future?
Number of cores may reach 1000 in the near future
Both the point to point interconnects and the NOCs will fail to scale
Both in terms of latency and bandwidth

## Slide 3: Hold on.. I said 1000 cores!!
Corona, Rigel, ATAC

## Slide 4: One-to-One or NOC?
One to one interconnection is clumsy(Multiple layers)
NOC
  Too many hops

## Slide 5: Applications of On-Chip Network
Cache coherence
  Invalidation Signals
Barriers
  Release signals
Cache bank communication
Communication between processors, memory controller and I/O devices

## Slide 6: Do We Need Optical Communication?
Less Delay
High Bandwidth
Optical
Server using On-chip nanophotonics by 2022

## Slide 7: Optical Communication
Fast
High bandwidth
High static power consumption

## Slide 8: Prior Works
Important Proposals
  Corona
  Firefly
  ATAC
  Probe

## Slide 9: Thesis Outline
Part I: Basics of on-chip optical interconnects
Part III: Application of the reconfigurable optical network
Part IV: Advanced network architecture
Chapter 6: Optical Overlay NUCA
Part II : Improvements in design methodology
Chapter 3: Enhancement in simulation infrastructure
Chapter 4: Efficient network synthesis and advanced network reconfiguration methods
Chapter 1: Introduction
Chapter 2: Background and literature survey
Chapter 5: Ultrafast optical components
Chapter 7: Energy efficiency (ColdBus)
Chapter 8: Scalability (BigBus)

## Slide 10
Part II : Improvements in design methodology
Chapter 3: Enhancement in simulation infrastructure
Chapter 4: Efficient network synthesis and advanced network reconfiguration methods
Chapter 5: Ultrafast optical components
Part I: Basics of on-chip optical interconnects
Part III: Application of the reconfigurable optical network
Part IV: Advanced network architecture
Chapter 6: Optical Overlay NUCA
Part II : Improvements in design methodology
Chapter 3: Enhancement in simulation infrastructure
Chapter 4: Efficient network synthesis and advanced network reconfiguration methods
Chapter 1: Introduction
Chapter 2: Background and literature survey
Chapter 5: Ultrafast optical components
Chapter 7: Energy efficiency (ColdBus)
Chapter 8: Scalability (BigBus)

## Slide 11: Enhancement in simulation infrastructure
To design an optical network, we have to characterize the optical properties of its basic components.
Designed a component library using RSoft CAD tool
Published these components as an open source library named OptiKit[*] (www.cse.iitd.ac.in/~srsarangi/softwares.html)
[*] OptiKit: An Open Source Kit for Simulation of On-Chip Optical Components Eldhose Peter, Smruti R Sarangi 27th International Conference on VLSI Design and 13th International Conference on Embedded Systems 2014, Mumbai

## Slide 12: Components I
MMI(Multimode Interference coupler)
Directional Coupler

## Slide 13: Components II
Microring resonator
Y Junction

## Slide 14
Part II : Improvements in design methodology
Chapter 3: Enhancement in simulation infrastructure
Chapter 4: Efficient network synthesis and advanced network reconfiguration methods
Chapter 5: Ultrafast optical components

## Slide 15: Understand the problem – Single Write Multi Read Bus
……….
Stations
SWMR Bus
Splitter
λ = split ratio
β = splitter loss
x
λβx
(1-λ)βx
(1-λ) λ β2x
(1-λ) 2 β2x
……….
(1-λ)(i-1)β(i-1)x
(1-λ)(i-2)β(i-1)λx
Splitter loss is exponential

## Slide 16: Where are we now?
Exponential time algorithm
Binzhang et al
Suboptimal algorithm
ATAC, Probe
Tree network
Reduces the variance
Theoretical split ratios (1/n, 1/(n-1)….1/4,1/3,1/2)

## Slide 17: SWMR
Same split ratio
β(n-1)(1-λ) (n-2) λy ≥ 1
When β = 1, optimal value of λ = 1/(n-1)
Power Utilization Efficiency =
= (1 -
2.718 times
1/2
1/3
…..
1/(n-1)
When β = 0
ATAC and Probe
Same split ratio
Different split ratio

## Slide 18: Split Ratio v/s Splitter Loss
β = Ϝ(λi)
200+ candidate designs
Y and DC splitters
Envelope

## Slide 19: Different Split Ratios –Linear Time Algorithm
Ϝ(λi) λiyi≥ Ai
Ϝ(λi) (1-λi ) yi ≥ yi-1
i-1 stations
ith station
Ϝ(λi) λiyi
Ϝ(λi) (1-λi ) yi

## Slide 20: SWMR- Tree

## Slide 21: Tree Algorithm
Left sub-tree
Right sub-tree
Combine the results
1 → M Splitters
Heterogeneous Splitters

## Slide 22: Tunable Splitters
Hardware Implementation
Ring
Tree
…..
Inactive
MMI and Microring resonator based tunable splitters
18 nm technology
Frequency divider(clock)
Cacti 5.3 simulations

## Slide 23: Ring
Phase 1
Leaf level
4 cycle
Phase 2
Non leaf level
28 cycles
=> 16 stations in 1 cycle
=> 64 stations in 4 cycles
Tree

## Slide 24: How our work differs?[*]
Linear time optimal dynamic algorithm
Solution is extended for trees and multilevel networks
Considers the relationship between splitter loss and split ratio
Provides solution in hardware for tunable splitters
Scalable for large number of nodes
Energy consumption of ring reduces by 87% and of tree by 90%
[*] Optimal Power Efficient Photonic SWMR Buses Eldhose Peter, Smruti R Sarangi SiPhotonics Workshop in High Performance and Embedded Architecture and Compilation (HiPEAC) 2015, Amsterdam, NETHERLANDS

## Slide 25
Part II : Improvements in design methodology
Chapter 3: Enhancement in simulation infrastructure
Chapter 4: Efficient network synthesis and advanced network reconfiguration methods
Chapter 5: Ultrafast optical components

## Slide 26: Microring Based Splitter[*]
In resonance
Out of resonance
Partial resonance
[*] Active Microring Based Tunable Optical Power Splitters Eldhose Peter, Arun Thomas, Anuj Dhawan, Smruti R Sarangi Elsevier transactions on optics communication
In
Drop
Through

## Slide 27: Active Microring Resonator
Changes refractive index => resonant wavelength

## Slide 28: High Split Ratio
15% - 85%

## Slide 29: Alternate designs
Array of resonators with different temperatures
Array of resonators with different sizes
Activate one at a time
Rings with different split ratios

## Slide 30
Part III: Application of the reconfigurable optical network
  Chapter 6: Optical Overlay NUCA
[*] Optical Overlay NUCA: A High Speed Substrate for Shared L2 Caches Eldhose Peter, Anuj Arora, Akriti Bagaria, Smruti R Sarangi,
21st annual IEEE International Conference on High Performance Computing (HiPC) 2014, Goa
&
Transactions on Parallel and Distributed Systems – TPDS (Submitted)
Part I: Basics of on-chip optical interconnects
Part III: Application of the reconfigurable optical network
Part IV: Advanced network architecture
Chapter 6: Optical Overlay NUCA
Part II : Improvements in design methodology
Chapter 3: Enhancement in simulation infrastructure
Chapter 4: Efficient network synthesis and advanced network reconfiguration methods
Chapter 1: Introduction
Chapter 2: Background and literature survey
Chapter 5: Ultrafast optical components
Chapter 7: Energy efficiency (ColdBus)
Chapter 8: Scalability (BigBus)

## Slide 31: Understand the problem - Cache
L1
L2
Lower Level Memory
L2
L2
L2
L2
L2
L2
L2
L2
UCA
NUCA
Sets
Improved cache utilization
Static => Not adaptable based on access pattern
Cache performance α 1/(hit latency)
Cache performance α hit rate

## Slide 32: Understand the problem – Optical Communication
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
50-60 cycles
1-2 cycles
Electrical
Optical

## Slide 33: Prior Approaches
No prior work in cache using optical NOC
Electrical NOC
  SNUCA
  DNUCA
  RNUCA
L1
Lower Level Memory
L2
L2
L2
L2
L2
L2
L2
L2
Search
Migration near to the core
111010101110001
1000
100011
Tag
Set Index
Block Size
1000
HomeBank
10100

## Slide 34: Equidistant nodes
Banks are equidistant in terms of delay(approx)
Dynamic creation of sets
  Improves the utilization of banks
    Improves hit rate
S
X cycles
X cycles
I am near to S
I am also near to S

## Slide 35: Phases of operation
Phase 1: SNUCA + Profiling
Phase 2 : Reconfiguration
Phase 3 : OONUCA
Then Phase 2, Phase 3, Phase 2, Phase 3 and so on

## Slide 36: Optical Overlay
Profiling information – Cache bank accesses, bank contention, cache lines used

## Slide 37: Creation of overlay
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
31
32
4
5
6
7
10
12
13
14
15
17
19
20
23
8
25
26
28
29
30
31
32
11
16
3
High
Low
Hybrid
Infreq

## Slide 38: TSI, BCAST and OP_BCAST
2
23
27
15
18
20
5
31
Home Bank
Broadcast
Two-Side Incremental (TSI)
27
23
20
5
2
15
18
31
Home Bank
OP_BCAST
Base Bank set
Overflow Bank set

## Slide 39: Home Bank Controller
Message Queue
NACK controller
Full
NACK Message
Search Logic
Search Bank
Read/Write
Fill Bank
Cache Bank
Read/Write
Response
Victim Buffer
Miss
Overlay Info store
Forward request to other banks
Message ID | Block Addr | MRBV
Miss
Eviction Logic
Hit
Evicted block
Migrate block
Response to the sender
Main Memory
Main memory Write
Main memory Read
Notify
Hit
Kill controller
Kill
To core
Response Collection Buffer

## Slide 40: Reconfiguration
2048 cache lines => 128 cycles
1033 µm2
Cadence tool

## Slide 41: Message Structure
Control Message
1 Flit – 3 cycles
Data Message
5 Flits – 7 cycles
NACK, Kill, Notify
Request, Response

## Slide 42: Architecture
32 cores and 32 cache banks
Clustered architecture – 16 stations
Distribute directory
Off chip laser

## Slide 43: What we achieved
Flexible and efficient access mechanism for large shared L2 caches
Mean speedup of 34% over SNUCA and 7% over TSI
Periodic network reconfiguration mechanism based on program characteristics
Number of bank accesses in OP_BCAST is reduced by 33% compared to broadcast
Proposal is agnostic to the network topology

## Slide 44
Part IV: Advanced network architecture
Chapter 7: Energy efficiency (ColdBus)
Chapter 8: Scalability (BigBus)
Part I: Basics of on-chip optical interconnects
Part III: Application of the reconfigurable optical network
Part IV: Advanced network architecture
Chapter 6: Optical Overlay NUCA
Part II : Improvements in design methodology
Chapter 3: Enhancement in simulation infrastructure
Chapter 4: Efficient network synthesis and advanced network reconfiguration methods
Chapter 1: Introduction
Chapter 2: Background and literature survey
Chapter 5: Ultrafast optical components
Chapter 7: Energy efficiency (ColdBus)
Chapter 8: Scalability (BigBus)

## Slide 45: Optical Communication - Detailed
The Laser is kept ON all the time
Nodes
Power Waveguide
Splitter
Data Waveguide
Draws
power
Modulated signal

## Slide 46: How to save static power consumption?
  Change laser output
  Inactive Stations
Laser modulation
  Multiple stations share the input laser power
Bandwidth sharing

## Slide 47: Laser Modulation
4
1
3
1
1
1
2
1
1:3
1:2
1:1
1:0
2
0:1
1:1
0:1
1:0
2
1
1

## Slide 48: Bandwidth Sharing
Power Waveguide
Arbitration Waveguide

## Slide 49: Where are we now?
Modulate Laser Power based on traffic
Reservation assisted SWMR
Share Bandwidth
Flexishare – stations are not active at a time
Ecolaser – turn laser on/off(without prediction)
Probe – link and buffer utilization based prediction
Pulse – predicts sharers of cache line
Wavelength stealing
Pairing of nodes
ColdBus
Backbone WG
Extra WG

## Slide 50: How our work differs?
A novel predictor for network activity
A mechanism to handle misprediction – Extra WG
A new laser modulation scheme with multiple DML lasers
Detailed bus design and reconfiguration
A technique to leverage both the laser modulation and bandwidth sharing
[*] ColdBus: A Near-Optimal Power Efficient Optical Bus Eldhose Peter, Arun Thomas, Anuj Dhawan, Smruti R Sarangi 22nd annual IEEE International Conference on High Performance Computing (HiPC) 2015

## Slide 51: Layout
Private L1
Shared L2
Array of 32 DML lasers
Fast Turn ON
Multiple output levels
Intracluster - Electrical
Intercluster - Optical
Coherence messages

## Slide 52: Operation
Reconfigu-
ration
Split ratio
Power
Normal
Phase
Draw power
Send message
Prediction
Backbone
Extra WG
An Epoch Duration

## Slide 53: Prediction & Reconfiguration
Address Based Prediction
Predict L1 miss in fetch stage
Extra Predictor
Based on the average wait time
Reconfiguration
Split ratio
If miss then Miss time predictor(out of order pipeline)
Laser power for the next epoch
To predict the epoch in which miss is going to happen
Mis-prediction by address based predictor
For the extra waveguide
For the backbone waveguide

## Slide 54: Working of ColdBus
Station Controller
Message Queue
Extra WG
Backbone
WG
Predictor WG
ERP WG
SWMR WG
Reservation
Channel
Resonator
Misprediction?
Couples light to another WG
Input Power
Data Transfer
Prediction

## Slide 55: Performance
Compared to the state of the art systems, ColdBus is
4.1X better in terms of power
3.1% faster
Shows 18% improvement in ED2

## Slide 56
Part IV: Advanced network architecture
Chapter 7: Energy efficiency (ColdBus)
Chapter 8: Scalability (BigBus)

## Slide 57: BigBus Architecture[*]
[*] OptiShare: A dynamic channel sharing scheme for power efficient on-chip optical interconnects Eldhose Peter, Smruti R Sarangi, Optics workshop in DATE 2016
[*] BigBus: A scalable optical interconnect Eldhose Peter, Smruti R Sarangi, HPCA (Submitted)
Division reduces
the number of
cascading nodes
Multiple lasers
1 laser=> 4 P-Cluster
Multiple levels reduces
the number of crossings
Partially shared data waveguide(O-Link)
Power sharing-
Reduces power consumption
The intelligent placement of cores and cache banks reduces the number of hops (O-Link and CB-Link)
CB Link
Prediction per P-Cluster

## Slide 58: Partially Shared O-Link
P-Cluster1
P-Cluster2
P-Cluster3
P-Cluster4
Power
waveguide
Data waveguide
P-Cluster 1
P-Cluster 2
P-Cluster 3
P-Cluster 4
1/4th of the bandwidth is assigned to each P-Cluster
Source: Anyone in P-Cluster 4
Destination: Anyone in the O-Cluster
O-Cluster

## Slide 59: Cache Bank Access
O-Cluster1
O-Cluster2
O-Cluster3
O-Cluster4
Dynamic Set Creation
Set =>1 Bank in every O-Cluster
No hub b/w O-Link & CB-Link

## Slide 60: Operation

## Slide 61: Message transfer
Station m
Station n
Token i
Token j
ith waveguide
jth waveguide
Power waveguides
in a p-cluster
Data
Waveguides
Token
waveguide
Modulate and
send on WG m
Modulate and
send on WG n
Token i & j
ith & jth
waveguide
Modulate and
send on WG i & j
Separate arbitration is not needed for the data waveguide
Any station can dynamically access a power waveguide

## Slide 62: What we achieved
A scalable optical interconnect
Prediction considers the number of pending events and average waiting time
Supports NUCA
Speedup of 14-55% and 9-56% reduction in ED2 compared to state of the art schemes
Intelligent placements of network element reduced number of hops for communication

## Slide 63: Conclusion
Created an optical network ab initio
Proposed optimal SWMR networks for all the commonly used topologies
Designed energy efficient and scalable on-chip optical interconnects
Used the efficient interconnect to implement a novel optical NUCA

## Slide 64: Let others do something!
Tunable splitters with a high range of split ratio
Power consumption can be reduced by improving prediction mechanism
Fairer arbitration schemes for BigBus
Mechanism to maintain the on-chip temperature
More applications

## Slide 65: Publications I
[J12] A survey on on chip optical interconnects Eldhose Peter, Smruti R Sarangi, (Ongoing)
[C11] BigBus: A scalable optical interconnect Eldhose Peter, Smruti R Sarangi, HPCA(Submitted)
[J10] Optical Overlay NUCA: A High Speed Substrate for Shared L2 Caches Eldhose Peter, Anuj Arora, Akriti Bagaria, Smruti R Sarangi, TDPS(Submitted)
[C9] OptiShare: A dynamic channel sharing scheme for power efficient on-chip optical interconnects Eldhose Peter, Smruti R Sarangi, Optics workshop in DATE 2016
[J8] Active Microring Based Tunable Optical Power Splitters Eldhose Peter, Arun Thomas, Anuj Dhawan, Smruti R Sarangi Elsevier transactions on optics communications
[A7] Fundamental Results for a Generic Implementation of Barriers using Optical Interconnects Sandeep Chandran, Eldhose Peter, Preeti R Panda, Smruti R Sarangi
[C6] A Generic Implementation of Barriers using Optical Interconnect Sandeep Chandran, Eldhose Peter, Preeti R Panda, Smruti R Sarangi 29th International Conference on VLSI Design, 2016, Culcutta, India

## Slide 66: Publications II
[C5] ColdBus: A Near-Optimal Power Efficient Optical Bus Eldhose Peter, Arun Thomas, Anuj Dhawan, Smruti R Sarangi 22nd annual IEEE International Conference on High Performance Computing 2015,
[C4] Tejas: A Java based Versatile Micro-architectural Simulator Smruti R Sarangi, Rajshekar Kalayappan, Prathmesh Kallurkar, Seep Goel and Eldhose Peter 25th International Workshop on Power and Timing Modeling, Optimization and Simulation,Salvador, Bahia, BRAZIL
[C3] Optimal Power Efficient Photonic SWMR Buses Eldhose Peter, Smruti R Sarangi SiPhotonics Workshop in High Performance and Embedded Architecture and Compilation 2015, Amsterdam, NETHERLANDS
[C2] Optical Overlay NUCA: A High Speed Substrate for Shared L2 Caches Eldhose Peter, Anuj Arora, Akriti Bagaria, Smruti R Sarangi 21st annual IEEE International Conference on High Performance Computing 2014, Goa
[C1] OptiKit: An Open Source Kit for Simulation of On-Chip Optical Components Eldhose Peter, Smruti R Sarangi 27th International Conference on VLSI Design and 13th International Conference on Embedded Systems 2014, Mumbai

## Slide 67
Thank You

## Slide 68: Splitter Assignment Problem for Trees
1 → M Splitters
Heterogeneous Splitters
50-50
0-100
100-0
AssignSplittersT

## Slide 69: Different Split Ratios –Linear Time Algorithm
…..
Assign Splitters
Split Ratio | β | λ

## Slide 70: Ring
4 Stations’ activity(4bits)
+ 8 bit power value
SR1 | SR2 | SR3 | SR4
212 Entries
85pS
32 bits
=> 16 stations in a cycle
Stations
=> 64 stations in 4 cycles
0
π/2
π
3π/2
400 pS
85 pS

## Slide 71: Tree – Phase 1
Leaf nodes
Power(8bits) | SR1(6bits) | …….. | SR7(6bits)
256 Entries
Phase 1
113pS = 1 cycle
8 at a time
Lookup table with 2 read ports
4 cycles for 8 rounds

## Slide 72: Tree – Phase 2
Power(8bits) | SR1(6bits) | …….. | SR7(6bits)
Phase 2
Reciprocal Cache
Div – 4 cycles
Access– 1 cycle
Multiplication for power – 2 cycles
=> 4 rounds = 28 cycles
2 Dividers
Single round
Single round
Two rounds
For N stations –

## Slide 73: Creation of overlay
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
31
32
4
5
6
7
10
12
13
14
15
17
19
20
23
8
25
26
28
29
30
31
32
11
16
3
High
Low
Hybrid
Infreq

## Slide 74: Operations in Overlay NUCA – Search
2
23
27
15
18
20
5
31
Home Bank
Broadcast
Two-Side Incremental (TSI)

## Slide 75: Operations in Overlay NUCA - Eviction
18
20
21
24
26
29
31
32
Home Bank
Main Memory
Eviction from L2

## Slide 76: TSI - Protocol
L1 Cache
L2 Cache Bank
If message type is request?
Miss
If space available in message queue?
No – NACK to sender(Exponential back off)
Yes - Search
Hit
Reply
If non home bank
  Kill to home bank
  Kill to opposite branch
Miss
Create Entry in RCB (Home bank)
Send request message to children
Notify message to home bank
Any Child?
Yes
No
Add notify
Remove entry from RCB
Type of Message ?
Notify
Kill
Home bank?
Yes
Remove entry from MQ
No
If notify = 2
Send request to Main memory
RCB |  | 
Entry |  | 
Miss
Hit
Remove RCB Entry
Remove MQ Entry
Miss
Notify

## Slide 77: Configuration
System
Cores – 32
L1 cache
Block size- 64 B
L2 cache
Banks – 32
Main memory
Latency – 250 cycles
Auxiliary Structures
RCB – 128
Technology – 18nm
Frequency – 3.4 GHz
Write mode – Write back
Size – 32 KB
MSHR - 32
Associativity – 8
Write mode – Write back
Size – 256 KB
Memory controllers – 4
MQ – 16
VB - 20
Laser – Off chip

## Slide 78: Results
Normalized Average Hit Latency
0.4-0.8
0.2-0.55

## Slide 79: Results
L2 Hit Rate
Comparable to DNUCA, much better than SNUCA
More home bank hits

## Slide 80: Results
Normalized IPC
2-3%
50, 24,18%
161%
167%
Less L2 requests
High non-home bank hits

## Slide 81: Laser Controller
Extra WG
ERP WG
Backbone WG
Predictor WG
To Directory
Off-chip
ON-chip
Tunable Splitter
Comb Splitter

## Slide 82: Station Controller
Station Controller
Message Queue
Extra WG
Backbone
WG
Predictor WG
ERP WG
SWMR WG
Reservation
Channel
Resonator
Misprediction?
Couples light to another WG
Input Power
Data Transfer
Prediction

## Slide 83: Evaluation
4.1
16.8
35
ColdBus
ArchLink
Parsec, Splash, Parboil

## Slide 84: Evaluation
Electrical
5
27.5
23
32

## Slide 85: Evaluation
0.8
0.32
0.39
0.48

## Slide 86: Dynamic Channel Sharing
Station m
Station n
Token i
Token j
ith waveguide
jth waveguide
Power waveguides
in a p-cluster
Data
Waveguides
Token
waveguide
Modulate and
send on WG m
Modulate and
send on WG n
Token i & j
ith & jth
waveguide
Modulate and
send on WG i & j
Separate arbitration is not needed for the data waveguide
Any station can dynamically access a power waveguide
Pending requests
Wait time
# of token = # of active waveguides
Tree + Bus power distribution n/w

## Slide 87: Results
No Laser Modulation – 1 token at a time
No Laser Modulation – Max. tokens
Dynamic Sharing - One token at a time
Multiple token at a time
14%
20-30X

## Slide 88: Optical Communication
Reservation assisted Single Write Multi Read(R-SWMR)
S
D1
D2
D3
Basic Components

## Slide 89: Introduction
Static Power Consumption
Laser is turned on all the time
Laser Modulation
Channel Sharing
Modulate laser(ecolaser)
Prediction (Probe, ColdBus)
Wavelength sharing
Channel Segmentation
Static schemes

## Slide 90: Performance

## Slide 91: SWMR- Different Split Ratios
1/2
1/3
…..
1/(n-1)
When β = 0
ATAC and Probe – SWMR-P

## Slide 92: SWMR and SWMR-S
Same split ratio
Different split ratio

## Slide 93: Evaluation
Split ratio – same
Splitter loss - 0.2 dB
Split ratio – same
Splitter loss - varies
Our Algorithm
3.73pJ
1.99pJ
Half
Not Scalable
81 pJ

## Slide 94: Evaluation
25%
120%
300%
0.1%
50%
87%
Multi Level

## Slide 95: MMI(Multimode Interference coupler)
The signal splits because of:
  Diffraction,
  Reflection off the walls
  Interference of the reflected waves
Needs to be designed delicately, and accurately.
Uses
  Beam splitter
  Optical multiplexer

## Slide 96: Directional Coupler
The signal in one waveguide couples with the adjacent waveguide
Coupling depends on
  Length of the parallel waveguide
  Separation between these waveguides.
Uses:
  Beam splitter

## Slide 97: Microring Resonator
A circular waveguide (ring) is placed between two straight waveguides
The optical signal first gets coupled
to the ring, and then to the other
waveguide. (a.k.a resonance)
Uses:
  (De)modulator
  Optical switch

## Slide 98: Y Junction
One waveguide splits into two
Split percentage depends on
  Split angle
  Width of the waveguide.
Uses:
  Beam splitter
  Optical multiplexer

## Slide 99: Parallel Waveguides
Coupling loss
Propagation loss
Coupling loss