## Slide 1: Computer Architecture: Past, Present, and Future
Prof. Smruti R. Sarangi
IIT Delhi

## Slide 2: What is computer architecture?
The study of computer processors and computer systems

## Slide 3: What does a computer do?
Almost everything:
  Financial calculations
  Games
  Weather forecasting
  Connect to friends on the other side of the world
  Astrology
  ...

## Slide 4: How does it do it?
Processor (CPU)
Mouse
Keyboard
Network
USB
Monitor
Printer
Hard disk
Brain of the computer system

## Slide 5
Past
Present
Future

## Slide 6: What does a program look like? Historical Perspective
Ever since mathematics was discovered
  Man always felt the need for a little bit more of help
Almost all early civilizations had accountants and book keepers
  They wrote simple programs (in their mind) to tally accounts, compute expenditures, and forecast future demands
This Photo by Unknown Author is licensed under CC BY-SA-NC

## Slide 7: Ancient Accountants
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 8: The first real computing machine – Abacus (simple and fast mathematics)
This Photo by Unknown Author is licensed under CC BY-NC-ND

## Slide 9: It is still being used!
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 10: Analog Computers
Wikimedia, Commons

## Slide 11: Basic operation
Can be used to compute the ratio r1/r2
Turn one gear r1 times, the other will turn r2 times

## Slide 12: Water computers: Could model the British economy
Source: wikipedia

## Slide 13: Basic Methods of Operation
Program
a = 100
b = 500
result = b / a
Computer
Output
Spend energy: move gears, move water, move electrons, move ...  get the result

## Slide 14: What was known about computing till 1900 AD
Task (program)
a = 100
b = 500
result = b / a
state
logic
a, b, result
+ - * / exp sin cos

## Slide 15: Then came Alan Turing and asked ...
What basic operations do we need to implement any kind of a program?

## Slide 16: Church Turing Thesis
A function is computable by a human being using an algorithm if and only if it is computable by a Turing machine
Tape head
Infinite Tape
read the
symbol
1
State Table
2
access the
state table
write a new
symbol
3
move the
tape head left or right
4

## Slide 17: Led to the design of the modern computer – Von Neumann, Eckert Mauchly, and others
CPU
Memory
I/O Devices

## Slide 18: We have the theoretical tools  How do we build a computer
Then came the transistor (1947, Bardeen and Brattain)
Simple 3 pin device.
Acts like a simple
electrically
controlled switch
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 19: By the 50s and 60s
Theoretical
Advancements
Technological
Advancements
Era of Computers

## Slide 20: Era of Big Computer Corporations
Gordon Moore (co-founder) of Intel proposed the Moore’s Law
The number of transistors per chip will double roughly every year
  Has held true for the last 55 years
  One year has increased to roughly 2 years

## Slide 21: Why does Moore’s law hold?
Transistors get smaller with every new generation
  1 micron in 1980 to 14nm in 2016
Smaller Transistors
High Speed
Lower Area
Lower Power

## Slide 22
Source: Wikipedia

## Slide 23: From 2000 to 2,000,000,000 transistors
What have we gained?
Performance
Clock Frequency  increased from 0.5 Mhz to 3 GHz (6000 times)
#instructions in a program  better compiler technology, reduced #insts by at least 2-3X in the last 30 years
IPC  Instructions per cycle
Performance
Equation

## Slide 24: IPC (Basis of Modern Computer Architecture)
In the steady state, the processor will take in n instructions every cycle (average), execute them, and complete them
The IPC is equal to n
Processor
Program
n
n

## Slide 25: What determines the IPC?
Pipeline
On-Chip Memory System
Off-Chip Memory System
Processor
Increase the #instructions
it can process per cycle
(average)
100s of techniques
Increase the hit rate (probability of finding data)
Decrease the access time and power
Increase the hit rate (probability of finding data)
Decrease the access time and power

## Slide 26: Crux of the techniques: Out of Order Execution
Processor
4
1
2
3

## Slide 27: Crux of the techniques: Speculation
Predict a value
Direction of a branch
Value of a variable
Dependence between instructions
Time it takes to access memory
Move ahead
If prediction is correct, GREAT
If prediction is wrong
Rollback and Recover

## Slide 28: Where did we reach with all these tricks ...
IBM 360
Early 60s
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 29: Modern Cellphone

## Slide 30: Which computer is faster, and by how many times ...
IBM 360
Samsung S5
10,000 times

## Slide 31
Past
Present
Future

## Slide 32: Processor Performance Scaling has reached its Limits
Clock frequency has remained constant for the last 10 years
6000
5
000
4000
3000
2000
1000
0
29/10/99
12/03/01
25/07/02
07/12/03
20/04/05
02/09/06
15/01/08
29/05/09
11/10/10
23/02/12
Date
Clock frequency (MHz)

## Slide 33: Processor Performance
Performance is also saturating
40
35
30
25
20
15
10
5
0
Speclnt 2006 Score
29/10/99
12/03/01
25/07/02
07/12/03
20/04/05
02/09/06
15/01/08
29/05/09
11/10/10
23/02/12
Date

## Slide 34: What stopped gains in processor performance?
Power and Temperature
  Power freq3
  We cannot increase frequency any more
This Photo by Unknown Author is licensed under CC BY-NC-ND

## Slide 35: What else?
IPC
  Diminishing returns ...
  Hard to handle localized temperature hot spots
Compiler Optimizations
  Again diminishing returns ...
Single core computer architecture is dead
This Photo by Unknown Author is licensed under CC BY

## Slide 36: New Mantra: Think parallel
Typical design of a multicore CPU
Cores
Cache banks
Memory
controller
Other
circuitry

## Slide 37: What are the new problems to be solved ...
Designing a parallel system
  Writing a parallel program
  Convert existing algorithms into parallel algos. or write new ones
  Design of parallel architectures
  Ease of programmability
  Sending messages between cores and cache banks effectively in such a system

## Slide 38: What about old friend power?
Tradeoff
  Performance per core
  Number of cores
  Frequency of each core
We can afford to have many low frequency cores
  As a result frequencies have come down in the past decade

## Slide 39: Novel methods of cooling  Water cooled server
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 40: Process Variation
Can you do fine grained calligraphy with a blunt knife  NO
Then, how can you design 14nm transistors with 193nm (wavelength) light?

## Slide 41: This is what you get ...
(courtesy: IBM Microelectronics)
bent, deformed shapes in silicon

## Slide 42: Process Variation Effects
Cannot accurately fabricate transistors anymore
Their power, and performance vary from specifications
Need to have a lot of error tolerance and timing margins
Create new variation tolerant architectures

## Slide 43: Reliability: Soft Errors and Hard Errors
Let us ask some questions:
We all know that it takes a lot of money to cool a super-computer. Why not place it on top of the Himalayas? No cooling required.
If I run a processor continuously for 10 years. What happens?

## Slide 44: You cannot place a supercomputer on mount Everest.
The processor will be bombed by cosmic rays
The resultant current pulse can flip bits

## Slide 45: What happens after 10 years of continuous operation ...
This is what happens to a wire after that many years  Electromigration
Designs should be tolerant to such ageing mechanisms
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 46: Security: The kill switch (HW Trojan)
September 2007: Israeli jets bombed a Syrian nuclear facility.
The Syrian radar had mysteriously stopped, but why?
  Scoop: Israelis sent a wireless message to the processor in the radar.
  It shut itself off.
  Research problem: How do you make a design tolerant to hardware Trojans.

## Slide 47
Past
Present
Future

## Slide 48: Transistor Size Roadmap
Year | Transistor Size
2016 | 14 nm
2018 | 10 nm
2020 | 7 nm
2022 | ???
It is not possible (?) to design such small transistors with current technologies.
7 nm = 70 atoms wide

## Slide 49: What next?
No Silicon
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 50: Future of Computer Architecture
Graphene – Sheet of carbon (1 atom wide)
Spintronics – Based on the spin of the electron
Quantum Computing – Store information as qubits  multiple bits at once
Instead of electrons use photons (light)

## Slide 51: Discussion on Teaching Computer Architecture
This Photo by Unknown Author is licensed under CC BY-SA-NC

## Slide 52: Contents of a basic course
Elements of a computer architecture course
Boolean Algebra
Assembly Languages
ARM
x86
Computer Arithmetic
Digital Logic
Representation of Numbers, Strings
Basic Course 1

## Slide 53: Contents - II
Elements of a computer architecture course
Processor Design
Memory Systems
Caches
Main memory
I/O Systems
Multiprocessors
Pipelining
Basic Course 2

## Slide 54
Available worldwide in stores in 2021.
Google books, Amazon, Flipkart.
Caches and
Main Memory
Out-of-Order
Pipelines
Processors for
Machine Learning
Theory of Memory
Models
GPUs
Security and
Low Power
Advanced Topics

## Slide 55
Thank You
srsarangi@cse.iitd.ac.in